Development of a Single-Carrier SM-MIMO Transceiver
System Concept
Literature Research

---
System Model SC-SM
Figure 1: General transceiver structure of SC-SM systems [1]

---
Spatial Modulation System Design
- Use ZP-aided SC-SM
  - BER performance
  - Only 1 Tx-RF chain
- Channel matrix might
  be rank deficient
- Trade-off amongst
  detection complexity, BER,
  achievable transmission
  rate and power efficiency
Figure 2: BER comparison of the ZP-aided SC-SM scheme over its CP-aided counterpart and various CP-aided classic MIMO transmission schemes [1]

---
Advantages & Disadvantages
Figure 3: A summary of main advantages and disadvantages of the SC-SM scheme [1]

---
Detector Design
- Conventional SM detectors focus on TA index, ignore ISI
- Conventional MIMO detectors assume N_r > N_t
- BER performance of GSM dominated by the detectors
- Receiver architectures:
  - Frequency-Domain Equalization
  - Time-Domain Equalization
  - Turbo Equalizer
- TDE-type detectors more attractive in context of SC-SM
- TDE detection schemes:
  - ML-based
  - Sphere decoding based
  - PIC-R-SIC
  - LSS

---
Low-Complexity Detection Scheme for GSM-SC
- Based on M-algorithm
- Single stream ML detection
- Avoids QR-decomposition
- Balanced trade-off:
  performance & complexity
- Scheme approaches ML
  detector with increasing M
- Efficient operation even in
  rank-deficient channel
  scenarios
Figure 4: BER of ZP-aided SM-SC and SM-OFDM with
different receiver antennas: (a) N_r = 1; (b) N_r = 2 [2]

---
Potential Design Issues
Figure 5: Potential future design issues and potential solutions [1]

---
Prospects
- Simulation of a single-carrier transmission system
- Addition of MIMO
- Addition of spatial modulation
- Proof of concept with GNU Radio

---
Any questions?
Sources
  - [1] P. Yang, Y. Xiao, Y. L. Guan, K. V. S. Hari, A. Chockalingam, S. Sugiura, H. Haas, M. Di Renzo, C. Masouros, Z. Liu, L. Xiao, S. Li and L. Hanzo, “Single-Carrier SM-MIMO: A Promising Design for Broadband Large-Scale Antenna Systems,” IEEE Commun. Surveys & Tutorials, vol. 18, no. 3, pp. 1687-1716, August 2016
  - [2] L. Xiao, D. Lilin, Y. Zhang, Y. Xiao, P. Yang and S. Li, “A low-complexity detection scheme for generalized spatial modulation aided single carrier systems,” IEEE Commun. Lett., vol. 19, no. 6, pp. 1069-1072, Jun. 2015
  - [3] Z. Tian, Z. Li, M. Zhou and X. Yang, “M-Algorithm-Based Optimal Detectors for Spatial Modulation,“ Journal of Commun., vol. 10, no. 4, April 2015
  - [4] L. Wei, c. Ming and S. Cheng, “An Improved QRD-M Algorithm in MIMO Communications,” Global Telecommunications Conference, 2007, IEEE GLOBECOM '07, November 2007