Development of a Single-Carrier SM-MIMO Transceiver
Detector Design
MIMO Implementation

---
System Model SC-SM
Figure 1: General transceiver structure of SC-SM systems [1]

---
Low-Complexity Detection Scheme for GSM-SC
- Based on M-algorithm
- Single stream ML detection
- Avoids QR-decomposition
- Balanced trade-off:
  performance & complexity
- Scheme approaches ML
  detector with increasing M
- Efficient operation even in
  rank-deficient channel
  scenarios
Figure 4: BER of ZP-aided SM-SC and SM-OFDM with
different receiver antennas: (a) N_r = 1; (b) N_r = 2 [1]

---
Current Detector Design
Transmission system fully implemented:
Channel Matrix scales according to N_t, N_r:

---
Current Detector Design
- Working MIMO implementation (N_t x N_r):
  - 1 x 2
  - 2 x 2
- M smallest metrics are chosen by M-algorithm:
  - M = 1
  - No final detection yet:
- Script to test the detector:
  - If every sent symbol is correctly detected: True
  - ~45% of the time this is the case (SNR = 10 dB)

---
Prospects
- Adjust sent symbols
- Generalize for number of multi-path links (P)
- Generalize for M (starting with M = 2)
- Compare BER performance with results in paper
- MIMO schemes to implement:
  - 2 x 1
  - N_t x N_r
- Fuse scripts: class based SISO transmission and MIMO detector scheme
- Addition of spatial modulation / spatial modulation symbols
- Proof of concept with GNU Radio

---
Any questions?
Sources
  - [1] L. Xiao, D. Lilin, Y. Zhang, Y. Xiao, P. Yang and S. Li, “A low-complexity detection scheme for generalized spatial modulation aided single carrier systems,” IEEE Commun. Lett., vol. 19, no. 6, pp. 1069-1072, Jun. 2015
  - >>> import this
  - >>> import antigravity