Development of a Single-Carrier SM-MIMO Transceiver for Broadband Large-Scale Antenna Systems
System Model & Analysis
Channel Estimation & Synchronization

---
System Model: Spatial Modulation
- Use antenna index information as additional modulation dimension.
- Apply information in specific SM-symbol modulation algorithm.
Figure 1: General structure of Spatial Modulation systems [0].

---
System Model: Large-Scale Single-Carrier
- Spatial Modulation predominantly investigated in flat fading channels.
- In frequency-selective channels: OFDM is assumed.
- Disadvantages of OFDM-SM:
  - Usage of various transmit antennas in one frame jeopardizes single-RF benefits of SM-MIMO.
  - Low power amplifier efficiency due to PAPR.
  - Computational burden of DFTs increases with number of transmit antennas
- Frequency-selective channel may be converted into frequency flat fading channels by carefully designed receive filters.
Figure 2: Comparison of PAPR of OFDM-SM and SC-SM [1].

---
Single-Carrier Spatial Modulation (1)
Figure 3: General transceiver structure of SC-SM systems [1].

---
Single-Carrier Spatial Modulation (2)
- Use ZP-aided SC-SM:
  - Promising BER
    performance.
  - Only one RF-chain
    at transmission.
- Channel matrix might
  be rank deficient.
- Attractive trade-off
  amongst detection
  complexity, BER,
  achievable transmission
  rate and power efficiency.
Figure 4: BER comparison of the ZP-aided SC-SM scheme over its CP-aided counterpart and various CP-aided classic MIMO transmission schemes [1].

---
Advantages & Disadvantages
Figure 5: A summary of main advantages and disadvantages of the SC-SM scheme [1].

---
Low-Complexity Detection Scheme for GSM-SC
- Based on M-algorithm
- Single stream ML detection
- Avoids QR-decomposition
- Balanced trade-off:
  performance & complexity
- Scheme approaches ML
  detector with increasing M
- Efficient operation even in
  rank-deficient channel
  scenarios
Figure 6: BER of ZP-aided SM-SC and SM-OFDM with
different receiver antennas: (a) N_r = 1; (b) N_r = 2 [2].

---
Specific Detector Design
Transmission system model:
For each step: compute and choose M best metrics.
Final detection after K steps:

---
Potential Design Issues
Figure 7: Potential future design issues and potential solutions [1].

---
Classic Channel Estimation scheme
- For each transmission antenna: send training sequence.
- Using Gold Sequences: no multi-path effects for different antennas.
  - A frame can contain multiple antenna sequences.
- Correlate with the corresponding sequence at the receiver.
  - Channel Impulse Response for each transmit antenna.
- Reconstruct channel matrix with impulse responses.
- Performance trade-offs:
  - Longer sequences → lower threshold for reconstruction & more overhead.
  - More N_t → more index information & more overhead.
  - More N_r → lower channel estimation SNR needed.

---
Simulation Results: Classic Approach (1)
Figure 8: Results of correlation: Channel Impulse Response for different sending antennas [N_r =2; N_r = 2; hard coded].

---
Simultaneous Frame Synchronization and Channel Estimation scheme
Figure 9: Proposed Synchronization & Channel Estimation scheme.

---
Simulation Results: Pulse shaped chirp
Figure 10: Upsampled frames: C and C’.

---
Simulation Results: SIMO / Split (1)
Figure 11: Cross-correlation of the received frame with C’ - split reception antennas.

---
Simulation Results: SIMO / Split (2)
Figure 12: Polyphase-cross-correlation of the received frame with C’ -
split reception antennas – split transmit antennas.

---
Frequency & Phase Synchronization
- Estimate frequency-offset by multiplying the identical values of the training frame halves:
  - Resulting phase-offset over time between points is frequency offset.
- Frame offset is estimated by energy of channel impulse response.
- Phase-offset is phase of frame begin of correlation.
Figure 13: Phase of the received frame.

---
Results
- Single-carrier SM and detector scheme:
  - System scales well.
  - Relatively low complexity.
  - Robust even in demanding scenarios.
  - Promising candidate for large-scale MIMO aided multiuser uplink and downlink design.
- Channel estimation and synchronization scheme:
  - Works well in most scenarios.
  - Overhead trade-off: frame length and coherence time.
  - Scheme might be published in a paper.

---
Prospects
- Current work:
  - Exhaustive tests and comparisons.
  - Test different channel models (COST, LTE).
  - Compare to other Spatial Modulation approaches.
  - Generalize, optimize and improve code base.
- In future works:
  - Proof of concept with GNU Radio.
  - Tests on hardware.

---
Any questions?
- Sources
  - [0] E. Basar, M. Wen, R. Mesleh, M. Di Renzo, Y. Xiao, H. Haas, “Index Modulation Techniques for Next-Generation Wireless Networks,” IEEE Access, vol. 5, August 2017
  - [1] P. Yang, Y. Xiao, Y. L. Guan, K. V. S. Hari, A. Chockalingam, S. Sugiura, H. Haas, M. Di Renzo, C. Masouros, Z. Liu, L. Xiao, S. Li and L. Hanzo, “Single-Carrier SM-MIMO: A Promising Design for Broadband Large-Scale Antenna Systems,” IEEE Commun. Surveys & Tutorials, vol. 18, no. 3, pp. 1687-1716, August 2016
  - [2] L. Xiao, D. Lilin, Y. Zhang, Y. Xiao, P. Yang and S. Li, “A low-complexity detection scheme for generalized spatial modulation aided single carrier systems,” IEEE Commun. Lett., vol. 19, no. 6, pp. 1069-1072, Jun. 2015